## Slide 1
Problem Statement
At a blind, obstructed intersection, a building blocks the line of sight between an approaching vehicle and a pedestrian or cyclist. Cameras, radar, and LiDAR need direct line of sight. SENTRY senses hazards beyond it, without a second powered sensor per corner.
Objective
Develop a roadside unit transmitting one OTFS waveform for sensing and communication.
Use a hybrid RIS to redirect the signal around the blind corner.
Classify the reflected signal and compute Time-to-Collision.
Deliver a prioritized hazard alert via C-V2X (Uu + PC5).
System Model
Roadside Unit → Transmits OTFS-encoded signal.
Hybrid RIS → Redirects signal around obstruction.
Edge AI → Classifies hazard, computes Time-to-Collision.
O-RAN Near-RT RIC → Delivers prioritized alert to vehicle.
Hardware/software requirements
Software-defined radio (SDR) platform for OTFS waveform generation
Sionna for OTFS waveform simulation and RIS ray tracing
128-element Active-Reflection RIS panel
Edge AI on college MEC server with TensorRT
O-RAN Near-RT RIC-compatible network stack
Dual-path V2X delivery (cellular Uu + PC5 sidelink)
SENTRY: 6G ISAC for Non-Line-of-Sight Road Safety
Team CacheMe — Aryan Iyengar (Waveform); Mou (RIS); Om Goyal (Edge AI); Faculty mentor: [Add name]
Methodology
Simulate OTFS vs OFDM performance under vehicular Doppler shift (Simulation A).
Model RIS coverage across the blind intersection using an SNR heatmap (Simulation B).
Pre-code the roadside unit's transmission using known intersection geometry.
Classify the reflected echo via micro-Doppler signature and compute Time-to-Collision.
Broadcast the alert via C-V2X (Uu + PC5), prioritized by O-RAN Near-RT RIC.
Result and discussion
• OTFS resists Doppler shift; OFDM's error rate exceeds 70%.
• Simulated 8.7 ms sense-to-act latency across five stages.
• RIS coherent gain recovers most of the ~45 dB blockage penalty.
• Open gaps: fractional-Doppler validation, hardware profiling.
• Hybrid RIS active elements could double as a local angle-of-arrival sensor (future work).